## Slide 1
CPS-IDS
AI/ML-Driven Intrusion Detection for Cyber-Physical Systems
CITY3116 — Advanced Computer Forensics | 2025–26

## Slide 2
CPS Testbed Architecture
Physical Arduino plant + software simulation (Purdue model)
Level 3 — SCADA PC / IDS / Attacker │ Ethernet (Modbus TCP) Level 2 — TP-Link LS1005G Switch │ ├─ PLC 1 (Mega + W5500) 192.168.1.20 │ │ RS-485 (Modbus RTU) └─ PLC 2 (Uno + MAX485) │ Level 1 — Control Logic │ Level 0 — Sensors & Actuators
• PLC 1 (Arduino Mega): Modbus TCP server, pump/valve control, RFID auth, LCD HMI
• PLC 2 (Arduino Uno): Modbus RTU slave, 5 sensors (ultrasonic, temp, sound, motion, water)
• Software twin: MiniCPS/pymodbus simulation with identical register map and control logic
• Plant dashboard: FastAPI + WebSocket GUI with live SVG visualisation and attack terminal
• Control logic: pump ON < 30%, OFF > 85%; valve synced; temp alarm > 40°C

## Slide 3
Multi-Layer IDS Design
Implemented in Rust (6-crate workspace) for memory safety and performance
20
Rule Engine Rules SYN flood, port scan, Modbus abuse, injection
2
Modbus Analysers Write-rate anomaly Read flood detection
6
CPS Physics Checks Register bounds, pump oscillation, spoofing
3
ML Models Random Forest, CNN+LSTM Isolation Forest
Detection Pipeline: Rule Engine → Modbus Analysis → CPS Physics → CNN+LSTM Inference
• ids-common: shared types, config, errors
• ids-collector: packet capture, flow tracking
• ids-preprocess: dataset loaders, SMOTE, scaling
• ids-engine: models, rules, ML inference, binaries
• ids-response: alerter, blocker, SIEM export
• ids-dashboard: web UI stub (axum)

## Slide 4
AI/ML Model Architecture
3 complementary models trained on 3 public datasets
CNN+LSTM (~297K parameters)
• Conv1d → ReLU → BatchNorm → Conv1d (feature extraction)
• LSTM: 2 layers, 128 hidden units (temporal patterns)
• FC: 128 → 64 → 5 classes, dropout 0.3
• PyTorch training → ONNX export for live inference
• Early stopping with patience=5, LR decay on plateau
Ensemble (RF + Isolation Forest)
• Random Forest: 100 trees, max depth 20 (supervised)
• Isolation Forest: anomaly detection for zero-days (unsupervised)
• Hard voting: 70% RF / 30% IForest weighted blend
Class | Category | Example Attacks
0 | Normal | Benign traffic
1 | DoS | DDoS, SYN flood, Slowloris
2 | Probe | Port scan, reconnaissance
3 | R2L | Brute force, web attacks
4 | U2R | Buffer overflow, rootkit
Training Datasets
Model | Dataset | Year | Features | SMOTE
A | NSL-KDD | 1999 | 122 | Yes
B | CIC-IDS2017 | 2017 | 78 | No
C | UNSW-NB15 | 2015 | 76 | Yes
D | Combined (A+B+C) | Mixed | 276 | No

## Slide 5
Training Results
Model | Dataset | Features | Random Forest | CNN+LSTM | Isolation Forest | RF+IForest | FPR
A | NSL-KDD | 122 | 67.26%* | 65.94%* | 77.24% | 67.26%* | 0.0301
B | CIC-IDS2017 | 78 | 99.73% | 99.83% | 81.37% | 99.73% | 0.0006
C | UNSW-NB15 | 76 | 93.90% | 92.95% | 82.50% | 93.84% | 0.0251
D | Combined | 276 | 97.80% | 97.67% | 80.20% | 97.82% | 0.0043
*Model A limited by NSL-KDD binary-only test labels (Probe/R2L/U2R collapsed)
99.83%
Best Accuracy CNN+LSTM, Model B
0.06%
False Positive Rate Model B
97.82%
Cross-Era Generalisation Ensemble, Model D

## Slide 6
Live IDS Monitor
Real-time packet capture, flow analysis, and ML inference
Architecture
• Rust binary captures packets via pnet (raw sockets)
• Bidirectional flow tracking with configurable timeout
• Extracts 78 CIC-IDS2017 features per completed flow
• Python subprocess runs ONNX model via JSON Lines IPC
• Time-windowed inference every 10s on active flows
CPS-Specific Detection
• Write-rate anomaly: >2.0 writes/sec triggers alert
• Read flood detection: >50 reads/sec flagged as DoS
• Physics engine: register bounds (valve 0–180°, tank 0–1023)
• Pump oscillation: detects Stuxnet-style rapid toggling (<5s)
• Sensor spoofing: flags direct writes to read-only registers
• State consistency: valve/pump mismatch, unsafe commands
~1ms
ML Inference Latency per prediction
10s
Inference Window Active flow analysis
Alert Output
• Structured JSON (alerts.jsonl) with severity levels
• Per-alert: category, confidence, model source, 5-tuple
• SIEM-ready: CEF/syslog export capability
• Graceful shutdown with final flow expiry and stats

## Slide 7
Forensic Investigation: Attack Scenario
8 attacks executed via automated pipeline (incl. Stuxnet MitM rootkit)
# | Attack | Modbus FC | Duration | Description
1 | Command Injection | FC 0x05 (Write Coil) | 45s | Forces pump ON/OFF every 5 seconds
2 | Pump Oscillation | FC 0x05 (Write Coil) | 45s | Rapid pump toggle every 2s (Stuxnet-style)
3 | Valve Manipulation | FC 0x06 (Write Reg) | 45s | Random valve positions (0–180°) every 3s
4 | Replay Attack | FC 0x05 (Write Coil) | 45s | Replays recorded ON/OFF command sequence
5 | Sensor Spoofing | FC 0x06 (Write Reg) | 45s | Writes fake tank levels (0–100) every 2s
6 | Modbus Flood (DoS) | FC 0x03 (Read Reg) | 20s | 100× read requests per iteration
7 | Multi-Stage | Mixed | 30s | Recon (10s) → manipulation (20s) → flood
8 | Stuxnet Rootkit (MitM) | Mixed | 60s | Intermittent actuator manipulation + sensor falsification
Evidence: pcap (tcpdump) | alerts.jsonl (IDS) | attack-manifest.json | system artifacts (processes, connections, PLC registers)

## Slide 8
Investigation Results
17
ML Alerts Across all 8 attacks
264
CPS Physics Alerts Oscillation, spoofing, mismatch
320
Write-Rate Alerts Modbus anomaly
13,109
Flood Detection DoS & multi-stage
Coverage
Attack | CPS | ML
Cmd Inject |  | ✓
Oscillation | ✓ | ✓
Valve Manip | ✓ | ✓
Replay | ✓ | ✓
Spoofing | ✓ | ✓
Flood |  | ✓
Multi-Stage | ✓ | ✓
Rootkit | ✓ | ✓
Forensic Tools & Evidence
• Wireshark: Modbus TCP dissector, FC filters, I/O graphs, conversation stats (14 screenshots)
• tcpdump: live packet capture on loopback port 5502 (3.5 MB, 38,289 packets)
• Custom IDS: 4-layer real-time detection (rules + rate + CPS physics + CNN+LSTM)
• System artifacts: 19 PLC register snapshots, process lists, network connections
• 100% attack coverage — all 8 attacks detected by ML; 6/8 by CPS physics engine

## Slide 9
Evaluation & Recommendations
Strengths
• CNN+LSTM achieves 99.83% accuracy with 0.06% FPR
• 4-layer defence-in-depth (rules + rate + CPS physics + ML)
• Cross-dataset generalisation at 97.8% (Model D)
• Real-time inference <1ms via ONNX Runtime
• Ensemble improves minority class recall (R2L +7%)
Limitations
• U2R class hardest (extremely rare training samples)
• Model A degraded by NSL-KDD binary test labels
• Domain gap: training data ≠ live Modbus traffic
• Rule engine generates false positives on localhost
Recommendations
• Domain adaptation: fine-tune on captured Modbus traffic
• Federated learning: train across CPS sites privately
• Adaptive thresholds: tune rule engine per deployment
• SIEM integration: CEF/syslog export for SOC workflows
Standards Alignment
• ISO 27001: A.12.4 logging, A.16 incident management
• IEC 62443: defence-in-depth for industrial control systems
• NIST CSF: Detect & Respond functions
• OWASP Top 10: injection prevention, access control

## Slide 10
Summary
6
Rust Crates
4
Model Variants
99.83%
Best Accuracy
8 / 8
Attacks Detected
• Built a complete CPS testbed (Arduino hardware + MiniCPS software simulation)
• Trained CNN+LSTM, Random Forest, and Isolation Forest on 3 public IDS datasets
• Deployed live IDS monitor with CPS physics engine and real-time ONNX inference (~1ms)
• Conducted forensic investigation detecting all 8 attacks (incl. Stuxnet MitM) across 4 layers
• Multi-layer approach compensates for individual model weaknesses — 100% attack coverage
Thank you — Questions?